## Slide 1: High Power RF and Distribution
John Reid / Accelerator Division
MaRie Team Visit
March 9, 2016

## Slide 2: Four High Power 1.3 GHz RF Systems at NML / FAST
  5 MWatt 1.3 GHz RF system for the RF Gun
    Klystron Thales TH2104C + Pulse Transformer
    Fermilab Bouncer Modulator & Charging Power Supply
    SPA WR650 5 Mwatt Isolator
    Fast Interlocks (PMT, FEP, FP,& RP) + PLC Interlocks (LCW, Temp, Vacuum, Cryo, Etc.)
  300KWatt 1.3 GHz RF system for Capture Cavity I (CCI)
    Valvo-Philips YK1240 300 kWatt klystron
    Fermilab Series Tube pulsed modulator & charging power supply
    Circulator + Dual directional couplers
    Fast interlocks (PMT, FEP, FP,& RP) & PLC interlocks (LCW, Temp, Vacuum, Cryo, Etc.)
  300 KWatt 1.3 GHz RF system for Capture Cavity II (CCII) –
    Valvo-Philips YK1240 300 kWatt klystron
    Fermilab Series Tube pulsed modulator & charging power supply
    Circulator + Dual directional couplers
    Fast interlocks (PMT, FEP, FP,& RP) & PLC interlocks (LCW, Temp, Vacuum, Cryo, Etc.)
  5 MWatt rf system for Cryomodule # 1 test – Can be upgraded to a 10MW klystron.
    Klystron Thales TH2104C + Pulse Transformer
    Fermilab Bouncer Modulator & Charging Power Supply
    SPA WR650 5 Mwatt Isolator
    Fast Interlocks (PMT, FEP, FP,& RP) + PLC Interlocks (LCW, Temp, Vacuum, Cryo, Etc.)

## Slide 3: 5 Mwatt 1.3GHz Thales TH2104C Klystron with Pulse Transformer, Oil Tank, & Waveguide Isolator
Waveguide
Isolator
TH2104C Klystron
Pulse Transformer + Oil Tank

## Slide 4: 5 Mwatt Klystron Modulator and Charging Supply
Charging Power Supply
Bouncer Modulator

## Slide 5: WR-650 Waveguide Distribution Twin Pack
SLAC Collaboration – Design & Deliver Distribution System
4 Twin Packs required for an 8 cavity cryomodule assembly
Hybrid
Circulator
High Power Phase Shifter

## Slide 6: FAST - 1.3 GHz Waveguide Distribution System

## Slide 7: 300 kWatt Modulator & Charging PS for YK1240 1.3GHz Klystron
Valvo-Philips YK1240 Klystron with Solenoid
Modulator + Charging Supply/Capacitor Bank

## Slide 8: LCLS-II Testing at CMTS
SSA’s with waveguide to cryomodule, one SSA per cavity

## Slide 9: Summary
Fermilab has designed, developed, and demonstrated high power 1.3GHz RF systems to operate SRF cavities at NML / FAST.
Worked with collaborators (SLAC) to develop waveguide distribution system for 8 cavity cryomodule for CM operation at NML / FAST.
High power RF for LCLS-II cryomodule testing at CMTS.
Expertise in high power RF systems