## Slide 1
Fermilab Control System
Jim Patrick - AD/Controls
MaRIE Meeting
March 9, 2016

## Slide 2: Controls Scope
Main Complex
Accelerator Test Facilities
NOvA experiment slow control system
Future Projects (PIP-II)

## Slide 3: Fermilab Control System (ACNET)
Unified system for the entire complex
  All accelerators, all machine and technical equipment
  Common console manager can launch any application
  Common software frameworks
  Common timing system
Three tier system
  Applications, central services, front-ends
Custom system developed for the Tevatron in early 80’s

## Slide 4: Fermilab Control System
Modular architecture
  Many major upgrades over the years w/same core architecture
  Almost all computers and much hardware
Supports simultaneous operation of variety of beam modes
  Timing system and much infrastructure to support this
Custom communication protocol (ACNET)
  Supports data request on any timing event (+delay)
  Supports blocks of high rate readings (Fast Time Plot request)
Custom timing system
  TCLK – event link
    Central Timeline Generator (TLG) + remotely generated events
  MDAT – “fast” data link

## Slide 5: Fermilab Accelerator Complex – Collider Era
NUMI
Recycler
miniBooNE
Tevatron
Main Injector
Linac
Booster
pbar
Fixed Target
e-cool

## Slide 6: Fermilab Control System
Front-ends
  Wide variety of hardware – CAMAC, VME, GPIB, Ethernet…
  Internet Rack Monitor – turnkey ADC, DAC, digital I/O package
  HRM front-end – Modernized IRM
  VME/VxWorks front-ends
  Java “Open Access Client” (OAC) front-ends
    Non-realtime, full Linux OS + database access
    For ethernet connected hardware, access groups of devices
  Labview front-ends (via OPC to Java OAC)
  Erlang language front-ends
    Recent development, mainly Ethernet connected hardware
    Also runs on Linux

## Slide 7: Fermilab Control System
Central (“Middle Layer”) Services
  Custom alarm system
  Data logging - ~80 parallel loggers
  Save/Restore, etc…
Applications
  “Parameter Pages”
  C/C++ based framework, (very) old graphics
  Java based framework – modern GUI
  Custom Accelerator Control Language (ACL)
Synoptic display – drag and drop builder
    Java based, view with Java application or web browser
    Adapted by RHIC/BNL

## Slide 8: Accelerator Test Facilities
High Intensity Neutrino Source (HINS)
  Low energy pulsed proton linac
  no longer active
Fermilab Accelerator Science & Technology facility (FAST)
  300 MeV ILC style SC electron linac
  IOTA ring under construction
Project X Injector Experiment (PXIE)
  CW capable SC proton linac
  Front end of future PIP-II accelerator

## Slide 9: Test Facility Control Systems
HINS and FAST started as independent EPICS systems
  Core tools + EDM and data archiver from SNS, …
  FAST was ILC test facility, other US labs expected to participate
ILC became unlikely, external participation never happened
Control systems were put under ACNET infrastructure
  Console manager, code management system
  EDM displays could speak ACNET as well as CA
EPICS parts all eventually ported to ACNET
PXIE is all ACNET
  Avoid older hardware and hardware platforms
  Avoid writing old graphics apps (use Synoptic, Java, scripts)

## Slide 10: NOvA Experiment Slow Controls
Detector power supplies
Rack and environmental monitoring
Two parts
  Part runs on data acquisition system hardware and buses
    EPICS – done by experiment DAQ group and not us
    IOCs with Control System Studio for user interface
  Remainder is ACNET and done by us
    All synoptic displays, no custom applications
    Independent installation in Minnesota – “ACNET in a Box”
  We wrote a gateway and do get some EPICS data into ACNET

## Slide 11: Future Projects & the Control System
PIP-II accelerator is a substantial controls project
Considerable infrastructure modernization is needed to support PIP-II and existing complex for decades to come
  Timing System
  Communication protocol
    Fully support EPICS front-ends?
  Hardware platforms – which new ones to support?
  Front-end processors and field equipment
  Middle layer services – alarms, logging etc.
    Exploring experiment DAQ system for waveform logging
  Application environment
PIP-II must interface well to the rest of the complex
  We can’t replace everything there all at once

## Slide 12: Summary
We support a large control system for the main complex with a variety of interleaved operational modes
It is a mostly custom system that originated in the early 80’s but has been continually upgraded since then
We have significant experience with EPICS
PIP-II + major upgrades to the current complex are planned
The control system must be upgraded for these new projects and to make the existing complex supportable for the future
Planning of these upgrades is underway
It is a good time to explore synergy with other projects