## Slide 1: 1.3 GHz and 3.9 GHz SRF Cryomodule Design and Engineering at Fermilab
Tom Peterson
Fermilab – Los Alamos MaRIE Project Meeting
March 9, 2016

## Slide 2: History of 1.3 GHz and 3.9 GHz SRF design experience
TESLA / ILC – 25 years since the start
  Fermilab was a major collaborator in the design of TESLA and in the ILC development effort
  Specifically for TESLA cryomodule and cryogenic system design – Tom Nicol, Tom Peterson
  More intensive effort on ILC over the past 10 years, more people at Fermilab involved in design
    ILC Reference Design Report (RDR) and Technical Design Report (TDR)
Long-standing close collaboration with DESY, INFN, CEA Saclay, and other laboratories for SRF continues today
Two 1.3 GHz cryomodules were built and tested: CM1 and CM2
  We have complete design packages for this version, essentially “Type 3+” (similar to XFEL) serving as ILC prototypes
  Design includes pressure vessel, vacuum vessel, and piping documentation and engineering analyses
Fermilab designed and built one 4-cavity 3.9 GHz cryomodule for DESY/FLASH; in operation for several years
  Collaborated then with INFN for the XFEL 3.9 GHz design
Fermilab developed and implemented SRF cavity pressure vessel standard (non-standard due to use of Nb, etc.) for CFR-851 compliance methodology

## Slide 3: Now – LCLS-II cryomodules – 1.3 GHz and 3.9 GHz
For LCLS-II, FNAL is responsible for cryomodule design
  Collaboration with Jlab and SLAC
Again, cooperation and assistance from DESY/XFEL and CEA Saclay extremely beneficial
1.3 GHz cryomodules for LCLS-II (35)
  Design is complete, assembly is underway
  Produce two streams of identical 1.3 GHz production CM at FNAL&JLab
    Tightly coordinated activity among partner labs
    Common procedures, common test performance database, common travelers, etc. (within infrastructure limits)
    Split procurements between the two labs
    Assembly of two prototypes in advance of 33 production cryomodules
    Test cryomodules prior to delivery to SLAC, including prototypes
3.9 GHz cryomodules (2)
  Under design now
  Brought back information from INFN / XFEL 8-cavity 3.9 GHz design
  Will be produced and tested at FNAL, following 1.3 GHz for efficiency
All cavities and cryomodules go in the linac
  1st two 1.3 GHz cryomodules (prototypes) must work to specification

## Slide 4: 1.3 GHz cryomodule designs at Fermilab
LCLS-II 1.3 GHz cryomodule – assembly underway now
CM2 (XFEL-style cryomodule – two built and tested)

## Slide 5: 1.3 GHz ILC prototype design (“T4CM”, Type 4 Cryomodule)
In the development of the TESLA / ILC / XFEL cryomodules there were four major design revisions, with some minor variations within each type
XFEL is a modified Type 3+
  Eight cavities, magnet at end, magnet at 2.0 K, conductively cooled current leads
ILC RDR and TDR designs envision a Type 4 cryomodule
  Sometimes referred to as “T4CM”
  Main feature change – magnet in the center
  No T4CM has been built
ILC T4CM cold mass (magnet in center)

## Slide 6: 3.9 GHz cryomodule design for LCLS-II at Fermilab
Design underway now. Based on both the XFEL 3.9 GHz design
and the LCLS-II 1.3 GHz design. Will be done this year.

## Slide 7: Fermilab cryomodule team for LCLS-II
The boxes above represent teams of people
Some key 1.3 / 3.9 GHz cryomodule engineers and designers not on chart above
  Yuriy Orlov – CAD model, detailed design, drawings management, procurements
  Yun He – engineering analyses, detailed design, integration with SLAC, and documentation for LCLS-II cryomodule (did the Cornell ERL mail linac cryomodule design)
  Joshua Kaluzny – cryo-mechanical engineering, instrumentation integration
  Matt Kramp – senior designer, CAD modeling, drawings
  Other experienced engineers and designers (Tom Nicol, low beta cryomodule team, others)