## Slide 1: Cryomodule Testing at Fermilab
E. Harms/Accelerator Division
MaRIE Team Visit
9 March 2016

## Slide 2: Introduction
Fermilab has grown its SRF infrastructure and become experienced in testing superconducting RF cryomodules
  Single cavity, e.g. CC-1, 2
  8-cavity cryomodules, e.g. CM-1, 2
  Some experience with e- operation
  Involvement with LCLS-II is allowing us to develop expertise in testing Cryomodules in a Production environment
  New testing facility at CMTF broadens our capabilities into the future

## Slide 3: NML/FAST
Originally conceived as an ILC test (with beam) area
  Operational 20 MeV electron injector - soon to be 55 MeV
  Operational 8-cavity TESLA style cryomodule (2nd one operated here)
  Build-up in progress to provide up to 300 MEV electrons, construct IOTA storage ring
Peak CM-2 Cavity Gradients with all 8 powered at once:
Sum = 258.1 MV, Average = 32.2 MV/m (pulsed)

## Slide 4: NML/FAST
Valuable experienced gained in
  Building a test cave (within an existing facility)
  Installing and operating a cryomodule
    Rigging & alignment
    Vacuum and cryogenics connections and leak checks
    Instrumentation/Interlocks
    Safety systems
    RF systems – low level and high power
    Controls including data management/archiving
    Developing test protocols
    Making repairs – including in situ ones
  CM-2 is the first cryomodule to meet the ILC gradient spec (average cavity gradient = 31.5 MV/m)

## Slide 5: CMTF/CMTS-1
Newest SRF test facility at Fermilab
Nearly ready for LCLS-II Cryomodule testing (April)
Main components include
  2 shielded test enclosures: CMTS-1, PIXIE
  Cryo plant (500 W @ 2 K) and distribution system
  Safety systems, Controls, Interlocks, LLRF, etc.
  High Level RF provided by SLAC
  Clean room

## Slide 6: CMTS-1
LCLS-II testing will require
  28-day testing turnaround (~11 days of cold operation)
  CW operation of cryomodules
  Low ambient magnetic environment
  Flexibility: both 1.3 & 3.9 GHz cryomodules
Test stand can be repurposed for future needs: PIP-II, etc.

## Slide 7: Summary
Fermilab has developed and demonstrated its ability to test fully-built cryomodules
Excellent performance achieved
Mature infrastructure in multiple locations
Capable and well-trained staff in the varied disciplines
Ramping up for LCLS-II Production testing will grow capabilities even more
This afternoon’s tour will allow you to see these facilities